## Slide 1
Hydrologic monitoring: Impact modelling & Climate Resilience
P. Donk & F.Kosso – 26 Nov. 2019 - Cayenne

## Slide 2: Hydrologic Monitoring: (Impact) modelling & Climate resilience

## Slide 3: Monitoring
Monitoring: Gauging networks
  MET Stations (Precipitation, Evaporation, Temperature)
  Hydraulic stations (River discharge)

## Slide 4: Hydrologic Modelling
Hydrologic modelling
  VHMbuild: Generalized Conceptual Model
  Parsimonious approach (Simplest effectively/efficiently fitting the purpose of application)
  Stepwise data mining based (sub)model structure identification & calibration procedure (=>high performance)
STORAGE
QUICK FLOW
ETo
P
DISCHARGE
VHM HYDROLOGICAL MODEL

## Slide 5: Hydrologic Modelling
Lumped conceptual => Sub-cathments => Watershed delineation (ArcGIS/ ArcMap/ QGIS)
STORAGE
QUICK FLOW
ETo
P
DISCHARGE
VHM HYDROLOGICAL MODEL

## Slide 6: Time Series processing/ analysis
WETSPRO
  WETSPRO: Water Engineering Time Series PROcessing Tool
  Supporting tool for VHM Model
  Stepwise (sub)model structure identification & calibration procedure

## Slide 7: Time Series processing/ analysis
WETSPRO
  WETSPRO: Water Engineering Time Series PROcessing Tool
  Extreme value distribution analysis
For example low flows:
Consideration of the duration of the low flow or drought period
→ discharge/duration/frequency relationships
→ considering different durations relevant for the several applications:
  irrigation
  hydropower plants
  domestic supply
  pollution

## Slide 8: Climate modelling: Climate Change Impact Assessments
Hydrologic response simulations/ river discharge
Analyzing climate change impacts
on water resources
Observed data
(pre-)processing
Climate modeling
Hydrologic modelling
Downscaling climate change scenarios

## Slide 9: Climate modelling: Climate Change Impact Assessments
Climate Perturbation Tool
(Statistical Downscaling of climate model outputs e.g. CMIP5)
  Precipitation
  Temperature
  Evaporation
  Wind

## Slide 10: Case study: Application to Suriname river basin/ Hydropower future impact assessments

## Slide 11: Case study: Application to Suriname Riverbasin/ Hydropower future impact assessments
Hydrologic response simulations/ river discharge
Analyzing climate change impacts on water resources, hence hydropower potential
Downscaling climate change scenarios
Observed data
(pre-)processing
Climate modeling
STORAGE
QUICK FLOW
ETo
P
Hydrologic modelling
BASE FLOW
DISCHARGE (FDC)

## Slide 12: Case study: Application to Suriname river basin/ Hydropower future impact assessments
UPPER SURINAME RIVER BASIN: DISCHARGE PROJECTIONS BY 2070-2100

## Slide 13: Case study: Application to Suriname river basin/ Hydropower future impact assessments
UPPER SURINAME RIVER BASIN: HYDROPOWER POTENTIAL PROJECTIONS BY 2070-2100

## Slide 14: Website
https://www.kuleuven.be/hydr/pwtools.htm

## Slide 15: Hydro-BID
Simulation tool created by IDB to support the management and planning of water resources use in Latin America and the Caribbean (LAC)
A system for integrated, quantitative simulation of hydrology and climate change for assessing the potential impacts of climate change on water flows and infrastructure and supporting the design of adaptive projects and strategies

## Slide 16: Hydro-BID: Components
Analytical Hydrography Dataset (AHD)
-Catchments and Stream network
Data input
-Precipitation , Temperature and Discharge
Hydrology Model

## Slide 17: Hydro-BID: Software
HydroBID from RTI international
Java Program to run climate interpolation and perform simulation
Sqlite Browser to view data of catchments: parameters, area, landuse, climate data
QGIS to view catchments and streams, to navigate, to identify waterside outlet COMID
Ms Excel to covert all sheet in CSV format

## Slide 18: Hydro-BID: Results after calibration

## Slide 19: Hydro-BID: Marouni basin
Chart: Discharge m3/s Station : Langa tabbetje Period : 1952 - 1982
| 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982
Max | 4290 | 5930 | 4670 | 5220 | 4630 | 5360 | 5270 | 3780 | 6570 | 3650 | 3900 | 6130 | 2900 | 3240 | 3870 | 5050 | 5635 | 6150 | 6080 | 5590 | 3500 | 4920 | 7460 | 6750 | 5020 | 4110 | 4750 | 5000 | 5540
Avg | 1507.1093 | 2041.9452 | 1697.0879 | 1930.7205 | 1910.9016 | 1738.9507 | 1102.163 | 1022.0282 | 1466.9891 | 1015.9479 | 1402.142 | 2232.6986 | 1006.8743 | 941.0795 | 1312.4141 | 935.4545 | 1757.7023 | 1814.1781 | 1560.4795 | 2282.25 | 1027.3228 | 1898.1566 | 1942.6603 | 2512.8142 | 1472.463 | 1468.7644 | 1623.3531 | 1526.2247 | 1908.8324
Min | 247 | 190 | 293 | 279 | 274 | 177 | 111 | 122 | 193 | 190 | 120 | 215 | 283 | 40 | 125 | 220 | 435 | 202 | 187 | 307 | 50 | 650 | 367 | 215 | 231 | 247 | 180 | 290 | 153
Chart: Waterlevel in cm NSP Station :8505 Langa tabbetje Period : 1952 - 1982
| 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982
Max | 886 | 1006 | 915 | 956 | 912 | 966 | 959 | 846 | 1050 | 835 | 855 | 1020 | 772 | 801 | 853 | 923 | 1013 | 1068 | 1028 | 991 | 1001 | 833 | 941 | 1126 | 1062 | 941 | 872 | 921 | 940 | 979
Avg | 628.8661 | 672.7205 | 646.1456 | 665.3507 | 669.0082 | 646.4685 | 573.7429 | 569.452 | 615.3361 | 572.7397 | 613.5341 | 692.7808 | 576.7787 | 549.7753 | 607.3098 | 568.2107 | 700.9088 | 689.8516 | 637.522 | 707.0595 | 666.8354 | 571.5049 | 683.1923 | 671.9973 | 715.6913 | 623.5781 | 625.1918 | 634.5424 | 626.9616 | 654.7041
Min | 465 | 450 | 475 | 472 | 471 | 446 | 422 | 427 | 451 | 450 | 426 | 457 | 473 | 375 | 428 | 437 | 543 | 469 | 423 | 473 | 459 | 366 | 542 | 489 | 457 | 461 | 465 | 447 | 439 | 432
Catchment Outlet COMID: 30116800
Total Catchment upstream : 663
Total drainage Area : 65781.27 sq km
Total stream segment length : 65781 km

## Slide 20
Ce support a été réalisé avec le soutien financier de l’Union Européenne.
Les opinions qu’il comporte n’engagent que sont auteur et ne reflètent pas nécessairement la position de l’Union Européenne.
Remerciements